## Slide 1: Ritz Carlton Hotel Riyadh-Saudi Arabia Irrigation water saving For Landscape Area

## Slide 2: Existing Sprayer Sprinkler
Irrigation water on walk ways and Asphalt road

## Slide 3: Existing Sprayer Sprinkler
Different type and model in irrigation system all with the same run time.
Water run time is not accurate with the different season and weather changes.

## Slide 4: Existing Sprayer Sprinkler
Dry areas , and many of Brown spots on Grass.

## Slide 5: Existing Sprayer Sprinkler
Wet areas.

## Slide 6: Replace using MP Rotator
Nov, 2015
Replacing the existing sprayer and gear rotors using the Matched precipitation Rotator to covers radius from 2.5 mtr. to 9 mtr.
applied to 3 Solenoid Valves.

## Slide 7: Existing different Nozzles
More than 150 Sprayers and 4 Rotors.
9 different types of Spry nozzles and rotors on small area.
Difficult in operation and future maintenance.

## Slide 8: Replaced MP Rotator Nozzles
MP Rotator Qty
MP 1000 90 ͦ-210 30
MP 2000 90 ͦ-210 ͦ 35
MP 3000 90 ͦ-210 ͦ 05
MP 3000 360 ͦ 03
MP 800 90 ͦ-210 ͦ 03
PR: 12 mm /hr

## Slide 9
Chart: Total Nozzles discharge per min.
| SP Total Flow G /min | MP Total Flow G /min
 | 232.68 | 60.68

## Slide 10: Irrigation Software to manage and monitor your system

## Slide 11: Using Solar Sync to Adjust The irrigation Run Time as per the weather condition.

## Slide 12: Station Activity

## Slide 13
Chart: Comparison between the discharge of MP rotator and Sprayer for 3 S.R.V.
| Dec-15 | Jan-16 | Feb-16 | Mar-16 | Apr-16 | May-16 | Jun-16 | Jul-16 | Aug-16 | Sep | Oct
SP Total Flow | 288523.2 | 288523.2 | 269908.8 | 288523.2 | 279216 | 288523.2 | 279216 | 288523.2 | 288523.2 | 279216 | 288523.2
MP Total Flow | 40127.684 | 147070.116 | 144585.27 | 144585.27 | 153796.494 | 262902.168 | 289443.6 | 293594.112 | 293594.112 | 288351.36 | 238517.91
Increased the valves run time as per Landscape Manager

## Slide 14
Chart: Comparison of Total Flow over 11 months
| SP Total Flow | MP Total Flow
Total Flow | 3117912 | 2058050.186

## Slide 15
MP Rotator in Operation
Sep 01 , 2016

## Slide 16
MP Rotator in Operation
Sep 01 , 2016
Healthy Grass ,
Dray curbstone and walk ways